## Slide 1: HLS Interface Synthesis

## Slide 2: Outline
Lab1 Block-level protocol
  Block-level和Port-level的差異
  介紹ap訊號
  解析波形圖
  ap_ctrl_none
Lab2 Port-level protocol
  Call by Value和Reference(address)
  可哪些設定ap訊號
  解析波形圖
Lab3 Array interface
  dual-port和single-port差異
  Array partition的相關設定介紹
Notes: 這裡是大綱
這次作業有4個lab
Lab1是block-level的protocol， 在這個lab中我會講解，究竟什麼是block level和port level
講解ap訊號代表意義
再來會從波形圖解釋ap訊號的功用
最後會告訴大家究竟什麼是ap_ctrl_none

## Slide 3: Outline
Lab4-AXI interface
  AXI-Stream和先前的單純array partition做比較
  解釋_hw.h檔的作用(AXIlite)

## Slide 4: Lab1 Block-level protocol

## Slide 5: Block-level和Port-level的差異
Block-level protocol
  針對block的控制訊號
Port-level protocol
  針對block IO的控制訊號

## Slide 6: 介紹ap訊號
ap_start(input)
  當訊號為1時，表示該block要”準備”開始運算
  須等ap_ready為1時，ap_start才可以為0。
ap_ready(output)
  收到ap_start為1並在資料讀取完後，ap_ready才會為1
ap_done(output)
  該block運算完，return數值有效時ap_done為1。
ap_idle(output)
  當block閒置時，ap_idle為1

## Slide 7: 波形圖

## Slide 8: Ap_ctrl_none
Cosim only supports the following ’ap_ctrl_none’
  Combinational design
  Pipeline design with task interval of 1
  Designs with array streaming or hls_stream ports

## Slide 9: Lab2 Port-level protocol

## Slide 10: Call by Value和Reference(address)
in1和in2為Call by Value
  僅為input
in_out1為Call by address
  可以做為input和output

## Slide 11: Call by value
ap_none | No I/O protocol. This is the default for inputs.
ap_stable | No I/O protocol.
ap_ack | Implemented with an associated output acknowledge port.
ap_vld | Implemented with an associated input valid port.
ap_hs | Implemented with both input valid and output acknowledge ports.
in1
in2

## Slide 12: Call by Reference
ap_none | No I/O protocol. This is the default for inputs.
ap_stable | No I/O protocol.
ap_ack | Implemented with an associated input acknowledge port.
ap_vld | Implemented with an associated output valid port. This is the default for outputs.
ap_ovld | Implemented with an associated output valid port (no valid port for the input part of any inout ports).
ap_hs | Implemented with both input valid port and output acknowledge ports
ap_fifo | A FIFO interface with associated output write and input FIFO full ports.
ap_bus | A Vivado HLS bus interface protocol.
In_out1

## Slide 13: 波形圖

## Slide 14: Lab3 Array interface

## Slide 15: 程式碼

## Slide 16: Dual-port和Single-port
Single-port(rolled-loop)
Dual-port(unrolled-loop)

## Slide 17: Single-port for input

## Slide 18: Dual-port和Single-port
Single-port
Dual-port
Dual-port的lantency為多少?

## Slide 19: Dual-port for input

## Slide 20: Dual-port for input and output

## Slide 21: Utilization

## Slide 22: Array partition
可將input或output的array分割成N個區塊並N個同時傳輸(N調整factor)
Type有block、cycle、complete

## Slide 23: Array partition
Input
  Dual-port
  Array partition type = block、factor=2
Output
  Ap_fifo
  Array partition type = block、factor=4

## Slide 24: 波形

## Slide 25: Type = complete for input and output
Compare report
波形

## Slide 26: Lab4 AXI interface

## Slide 27: Compare with Lab3
Lab4
  Interface = AXIS
  Array partition type = cycle, factor=8
Lab3
  Interface = ap_fifo
  Array partition type = cycle, factor=8

## Slide 28: _hw.h file

## Slide 29: Q&A